## Slide 1: Emerging technologies for WLAN
Oscar Osornio
Assignment 2

## Slide 2: Topics covered
802.11ac
  Larger Bandwidth
  Higher order modulation
  MIMO & MU-MIMO transmission modes
802.11ah
  Internet of Things market
802.11ai
  Fast network acquisition
802.11ax
  High-efficiency networking

## Slide 3: Introduction
Large growth in the WLAN market
  Public areas
  WLAN-enabled devices
Wireless streaming
  Audio
  Video
Increased demand equals emerging new technologies

## Slide 4: 802.11ac

## Slide 5: Key technical features
Mandated Use of 5GHz Band
  Larger spectrum
  Dual-band provides higher data rates
Maximum Data Rate
  Expanded channel bandwidth
  Higher-order modulation
  Peak data rate of 6.9 Gb/s
  Crossable 1 Gb/s threshold in small form-factor devices
Rate-Range
  Twice the range of previous devices
  Three times the peak rate performance
  Increased throughput in various scenarios
  Improved battery life
Eight Spatial Streams
  802.11n only used 4 SSs
  Data rate scales with MIMO channel dimension
Multi-User MIMO
  802.11n used SU-MIMO
  802.11ac use MU-MIMO
MU-MIMO Performance
  Max throughput at 75% SSs to antennas
  Low SINR for CSI feedback delay of 50 ms w/ handheld devices
  Low SINR for immediate CSI feedback w/ walking while on the phone

## Slide 6: 802.11ah
Internet of Things and Extended-Range WLAN

## Slide 7: Features & Supporting Measurements
Home automation includes temperature, moisture, and security sensors
Battery-powered and headless
  Require whole home coverage including attics, backyards, basements, and garages
Targeting lower-data-rate and longer-range applications
Specifically in the range below 1 GHz
1 & 2 MHz bandwidth modes that are globally interoperable
  Suited for devices that require low power consumption and long-range connection
Improved coverage and higher data rates in locations with larger path loss
Exploiting better range capabilities of 802.11ah allows for multiple-year battery operation
Favorable for outdoor use

## Slide 8: Emerging technologies

## Slide 9: 802.11ai
Optimized Connectivity Experience
  Faster initial link setup time
  FILS discovery framed defined
    More efficient and more frequent beacon transmissions
    More rapid network detection
  Neighbor AP advertisement
  Significantly reduced handset connection time

## Slide 10: 802.11ax
High-Efficiency WLAN
  Considers application trends with bidirectional, uplink-intensive, and peer-to-peer traffic such as:
    Video-conferencing
    User-generated uploads from wearable devices
    Smartphones and other consumer electronic devices
    Display
    Docking
    Scalable peer-to-peer networks
  Increase parallelization of traffic in the spatial and frequency domains